An individual configuration file is used to define each bandwidth control policy. This file specifies bandwidth limits for protocol classes (groups). The method is similar to overall bandwidth control).
fdpi_ctrl utility applies the configured policies to subscribers.
The format of the instruction:
fdpi_ctrl команда --policing файл_описания_полисинга [список_IP]
Instructions' syntax and IP addresses specification methods are described in details here: Control instructions.
The First Example:
We intend to offer our subscribers the plan for 10 Mb/s with torrent bandwidth limit of 3 Mb/s.
To accomplish the goal we create a class for torrents as described in Configuring priorities.
bittorrent cs1
default cs0
We split the traffic into 2 classes for this example:
cs0 - corresponds to DSCP=0 QOS(IPP)=0 Best Effort
cs1 - corresponds to DSCP=8 QOS(IPP)=1 Priority
We create the configuration file rateplan_1.cfg. It specifies bandwidth limits for each of 8 protocol classes (groups). We use HTB (the method of borrowing available bandwidth) and specify the bandwidth limit for torrents 3 Mb, but not smaller than 1 Mb. Unlike torrents, other traffic may take the whole available bandwidth.
htb_inbound_root=rate 10mbit
htb_inbound_class0=rate 8bit ceil 10mbit
htb_inbound_class1=rate 1mbit ceil 3mbit
htb_inbound_class2=rate 8bit ceil 10mbit
htb_inbound_class3=rate 8bit ceil 10mbit
htb_inbound_class4=rate 8bit ceil 10mbit
htb_inbound_class5=rate 8bit ceil 10mbit
htb_inbound_class6=rate 8bit ceil 10mbit
htb_inbound_class7=rate 8bit ceil 10mbit
htb_root=rate 10mbit
htb_class0=rate 8bit ceil 10mbit
htb_class1=rate 1mbit ceil 3mbit
htb_class2=rate 8bit ceil 10mbit
htb_class3=rate 8bit ceil 10mbit
htb_class4=rate 8bit ceil 10mbit
htb_class5=rate 8bit ceil 10mbit
htb_class6=rate 8bit ceil 10mbit
htb_class7=rate 8bit ceil 10mbit
htp_inbound_root, htb_root are the root classes that define the overall bandwidth for inbound and outbound traffic. The bandwidth is distributed within these classes.
rate - is the minimal bandwidth
ceil - is the maximum bandwidth that can be borrowed from the root class if available
class2-7 would not be used as we configure two classes only: 0 and 1.
Here we assign the configured policy to subscribers that use this plan:
fdpi_ctrl load --policing rateplan_1.cfg --file subscribers_with_rateplan_1.txt
The Second Example:
Let us assign the plan from the previous example to a subscriber with several IPs.
Check that BD support is enabled in dpi /etc/dpi/fastdpi.conf:
udr=1
If it is not enabled: we enable it and restart DPI: service fastdpi restart
We reserve for corporative subscriber all his IPs:
fdpi_ctrl load --bind_multi --user OOO_PizzaJohnes:192.168.0.1-192.168.0.5,192.168.1.10-192.168.1.25
The subscriber's IP list can be modified dynamically (i.e. add new IPs and delete it).
We assign the bandwidth limits according to the plan:
fdpi_ctrl load --policing rateplan_1.cfg --login OOO_PizzaJohnes
For advanced users: We advise to learn how to control outbound traffic via feedback loop.