# FastPCRF Management
The following are the fastPCRF commands, so you have to specify the fastPCRF address in the -r argument of the fdpi_cli utility.
## Connection to PCRF
### pcrf connect show
Displays the current status and accumulated statistics for connections to PCRF.
fdpi_cli -r <address> pcrf connect show
### pcrf connect switch [<pcrf_index>]
Forces connection to the specified PCRF
fdpi_cli -r <address> pcrf connect switch [<pcrf_index>]
where <pcrf_indxed> — the index of the connection line in the auth_server parameter. If <pcrf_indxed> is not specified — it defaults to 0.
## Authorization request queue
Authorization request queue - is an internal fastPCRF queue, which is designed to smooth out the peaks of calls to the Radius-server. When fastDPI authorization from fastPCRF, it does not take into account the bandwidth of Radius-server. There are parameters in fastpcrf.conf that set the maximum length and time spent in the queue, but sometimes you need to manually clear the queue or view its statistics.
### pcrf auth queue stat
Displays statistics on the internal queue of authorization requests:
fdpi_cli -r <address> pcrf auth queue stat
### pcrf auth queue clear
Clears the authorization queue. You can clear the entire queue with the command:
fdpi_cli -r <address> pcrf auth queue clear
or the oldest records by specifying the time = N parameter, where N is the number of seconds, - records older than the specified number of seconds will be removed from the queue:
fdpi_cli -r <address> pcrf auth queue clear time=60
## Persistent reply queue
Persistent queue management commands (fastPCRF response queues for authorization requests)
### pcrf persist queue stat
Displays persistent queue statistics for each fastDPI:
> fdpi_cli -r <address> pcrf persist queue stat Statistics of persist queue (pcrf -> fastdpi): FastDPI #0 '127.0.0.1%lo': queue file: /var/spool/dpi/pcrf/pq-127.0.0.1:29000 current: page count=1, item count=0 connected at: 2019/12/04 12:02:52, -25.332764s (13249164373261240 ticks) last sent: n/a (0 ticks) next reconnect: n/a (0 ticks) Statistics: sent: packet=0, bytes=0, error=0 received: bytes=0, error=0 socket: open=1, close=0, buffer overflow (split packet)=0 queue: enqueue packet=0 (0 bytes) drop head=0, push exception=0, clear count=0 FastDPI #1 '10.20.30.41%eth0': queue file: /var/spool/dpi/pcrf/pq-10.20.30.41:29000 current: page count=1, item count=3560 last sent: n/a (0 ticks) next reconnect: 2019/12/04 12:03:18, +0.705613s (13249242490512650 ticks) Statistics: sent: packet=0, bytes=0, error=0 received: bytes=0, error=0 socket: open=0, close=0, buffer overflow (split packet)=0 queue: enqueue packet=0 (0 bytes) drop head=0, push exception=0, clear count=0

### pcrf persist queue clear
Clears all queues or only the specified queue. The command response is the queue statistics after clearing.
# clears all queues fdpi_cli -r <address> pcrf persist queue clear # clears a queue by its number # the queue number can be found from the output of the pcrf persist queue stat command fdpi_cli -r <address> pcrf persist queue clear 1 # clears a queue by its name fdpi_cli -r <address> pcrf persist queue clear 127.0.0.1%lo

### pcrf persist queue reconnect
Allows you to reconnect to fastDPI without resetting the queue. It can be applied to a specific connection or to all.