# 9 PCRF Policy Server
PCRF provides proxying requests from fastDPI to the Radius server. It is a part of the standard Stingray Service Gateway installation package, but if necessary, it can be used as a dedicated server.
## Hardware Recommendations
In order to run PCRF you can use the following hardware or virtual machines matching the following characteristics:
1. CPU 2.5 GHz, 1 pcs
2. RAM 512 MB - 1 GB
3. HDD 50 GB - 250 GB
4. Operating system Cent OS 6.4+, 8+
5. NIC ranging from 10 Mb/s
## Installation
1. Install the Network Time Protocol daemon
  yum install ntp -y
  ntpdate pool.ntp.org
  service ntpd start
  chkconfig ntpd on
2. Add vasexperts repository
  rpm --import http://vasexperts.ru/centos/RPM-GPG-KEY-vasexperts.ru
  rpm -Uvh http://vasexperts.ru/centos/6/x86_64/vasexperts-repo-2-1.noarch.rpm
3. Install the fastPCRF
  yum install fastpcrf
4. Make sure the service is running
  service fastpcrf start
5. Сonfigure fastpcrf service to run at startup
  chkconfig fastpcrf on
6. Open firewall ports in order to access the fastDPI and Radius servers
  vi /etc/sysconfig/iptables
  -A INPUT -m state --state NEW -m tcp -p tcp --dport 22 -j ACCEPT
  #Radius
  -A INPUT -m state --state NEW -m udp -p udp --dport 1812 -j ACCEPT
  -A INPUT -m state --state NEW -m udp -p udp --dport 1813 -j ACCEPT
  -A INPUT -m state --state NEW -m udp -p udp --dport 3799 -j ACCEPT
  #fastDPI
  -A INPUT -m state --state NEW -m tcp -p tcp --dport 29002 -j ACCEPT
and restart firewall for the rules to take effect
service iptables restart
Disable selinux [1)]
[1)] temporary solution
setenforce 0
vi /etc/selinux/config
SELINUX=disabled