# Log Management with rsyslog
rsyslog is a service for managing system logs. It works as a daemon, providing tools to collect messages and send them to a storage location.
Functions of rsyslog:
- Receive messages
- Filter and sort messages — determine their priority and type
- Store messages — write them to specific files or forward them to a remote server
The system is highly configurable: you can set it to save any type of message to any file.
rsyslog can receive and transmit logs over the syslog protocol across a network, using both TCP and UDP through the standard port 514.
Scripts for integrating SCAT logs with syslog and systemd units for their execution:
- parser.bash — monitors SCAT logs and converts them to rsyslog format using the logger module.
- bng_logmon.service — systemd units to launch the scripts.
- bng.conf — an example configuration for sending logs to a remote server, which can be used as is or modified for more flexible settings.
## Requirements
- A running fastdpi process — it generates log entries, required for the SSG message-sending scripts.
- A running rsyslog daemon.
## Installation
Install bnglogmon:
yum install bnglogmon

2. Edit the file /etc/rsyslog.d/bng.conf — specify the server address and the sender’s IP address (if necessary, provide a specific IP).
3. Enable automatic startup of bnglogmon at system boot:
systemctl enable bnglogmon.service

## Execution
Start bnglogmon:
systemctl start bnglogmon.service

2. Restart rsyslog:
systemctl restart rsyslog.service

## Configuration
The rsyslog daemon is configured according to the settings described in its official documentation.