# Configuration
The option can be enabled in two ways:
1. Default profile: global configuration on the device, connected as a service without specifying a profile.
2. Named profile: connected as a service with the name of the profile.
For BRAS you have to use profiles named in the Radius-Accept attributes.

## Default profile
Enable the configuration parameter in /etc/dpi/fastdpi.conf for the default profile without a named one:
cp_server=192.168.0.18/cp

Here 192.168.0.18 — is the name or the address of the information page[1)].
[1)] additional parameters can be added (according to HTTP rules) only after ? or &, they must be specified in the URL for whitelisting and here you should think for DPI, otherwise DPI will assign /?
This address may include a (partial) path. This allows using the same server for various kinds of services.

After the parameter is added you need to restart the service:
service fastdpi restart

In this case management is carried out through connecting service 5 without specifying a profile:
fdpi_ctrl load --service 5 --ip 192.168.0.1 fdpi_ctrl load --service 5 --login user01

The white lists from /var/lib/dpi directory are used. Preparing white list

## Named profile
Find out how to configure the named profile in the next section.
## Additional settings
The maximum number of profiles for whitelists is set by the configuration parameter in etc/dpi/fastdpi.conf
for allow lists (service 5)
max_profiles_white_list=4

where 4 is the default value and 65535 is the maximum possible value
for allow lists (service 16)
max_profiles_serv16=32

where 32 is the default value and 65535 is the maximum possible value
This is a cold parameter and requires a restart of fastdpi.