1. In case your network driver can not be loaded after the kernel's update, you can try to resolve the issue by yourself:
ls /lib/modules/`uname -r`/extra
If kernel modules pf_ring.ko and igb.ko (or ixgbe.ko for 10G cards) are not present in this directory, please copy them from the similar directory of the previous kernel version:
find /lib/modules -name pf_ring.ko
cd path_found
cp pf_ring.ko /lib/modules/`uname -r`/extra
cp igb.ko /lib/modules/`uname -r`/extra # or ixgbe
and execute these instructions:
depmod -a
modprobe pf_ring
modprobe igb # or modprobe ixgbe
2. If your network card supports bypass functionality: you need to recover the bypass driver as well.
To find the driver:
find /lib/modules -name bpctl_mod\*
Copy it to extra:
cp bpctl_mod.ko /lib/modules/`uname -r`/extra
depmod -a
To verify operation:
bpctl_start
bpctl_util all get_bypass
Please contact tech support if these steps do not help.